商用型互联网自助式智能现磨咖啡饮品制作售货机 技术参数

SPECIFICATIONS OF

COMMERCIAL-TYPE INTERNET-BASED SELF SERVING SMART GROUND-COFFEE-MACHINE

基本参数

| 外形尺寸 dimensions | 宽W*深D*高H 1000* 850*1960 (mm) |
| --- | --- |
| 设备重量 weight | 220-260 KG |
| 安装电源 | AC110 – 220 V/ 50 Hz |
| 安装功率 capacity | 4000 W |
| 最大输出功率 max output | 2500 W |
| 待机耗电 standby power consumption | 2.0 – 4.0 KW/ 24 Hours |
| 通讯端口 Com | USB, WIFI, 4G, 3G, RS232 |

| 配件装置功能 Hardware | 系统名称 software |
| --- | --- |
| 设备硬件 hardware | 四桶水自动切换上水装置 4-bucket-water auto supply, swappable | 设备端系统 | 屏幕点单系统 front panel drink-ordering |
|  | 感应式独立上水水箱装置 Independent water supply, with sensor |  | 广告播放系统 Advertisement display system |
|  | 废水桶（水满）感应装置 waste water bucket, with sensor |  | 制作排队等待系统 Drink-making and waiting system |
|  | 桶装水预存放区（带锁） Bucket water storage area, with lock |  | 语音导购系统 Voice-guidance on auto sales |
|  | 感应式六工位制作装置 |  | 后台控制操作系统 Backstage Operation |
|  | 可调12-16OZ自动存杯落杯装置 Auto, cups storage and dropping, adjustable | 移动端用户购名操作系统 | LBS定位系统 LBS positioning |
|  | 自动下盖压盖装置 Auto, cap pressing and closing |  | 点单支付系统 payment on order system |
|  | 商用高品质咖啡磨豆装置、高压冲泡装置 High-quality coffee bean grounding and high-pressure brewing function |  | 饮品口味调整系统 Beverage flavor-adjustment system |
|  | 奶泡装置+4L鲜奶冷藏奶泡装置 Milk foaming + 4L fresh milk cold-storage |  | 用户分享、赠送系统 Consumers sharing, gifts system |
|  | 快速即热热水装置 Fast water boiling system |  | 饮品DIY 制作系统 Beverage DIY making system |
|  | 进口速溶冲泡搅拌装置（7个粉料盒+4个冲拌器） Imported instant coffee solving, brewing, stirring system (7 capsules, 4 brewers) |  | VIP 充值系统 VIP prepayment charging system |
|  | 自动制冰出冰装置（圆冰） Auto ice-making system (round-shaped ice cube) |  | 积分换购商城系统 Points and coupon for goods |
|  | 三套高品质精准浆料添加装置 3 sets of high quality flavors (e.g. vanilla flavor) feeding devices |  | 用户开店销售系统 |
|  | 五套高品质精准浆料添加装置 5 sets of high quality flavors feeding devices | 移动端管理系统 | 移动端运维工作管理系统 Mobile, operation and maintenance |
|  | 液晶触摸高清屏32” LED touch screen 32” |  | 移动端管理“看店”系统 Mobile, store-keeping |
|  | 咖啡豆现磨滚动展示区coffee bean grounding display | 云端后台管理系统 cloud-based backup management | 首页地图图形显示系统 Map displaying system, on page 1 |
|  | 二维码扫描取货装置 Drink supply by QR code scanning |  | 权限管理系统 Authorization assignment |
|  | 嵌入式工业级控制计算机 Embedded industry-level computer |  | 设备管理系统 Facilities management |
|  | 感应式出货取杯门 Sensored gate to open to take out drinks |  | 物料管理监督系统 Merchandise and consuming goods supervision system |
|  | 内置纸巾、打包袋存放抬取装置 Built-in Napkin, plastic bags storage and pickup |  | 加盟商业管理系统 Franchise management |
|  | 紫外线臭氧杀菌器 Ultraviolet ozone sterilization system |  | 个人认养系统 Individual caring system |
|  | 便携置物平台 内部照明灯 Potable tray, built-in lamp lighting |  | 财务管理系统 Financial management |
|  | 灯箱广告区 Advertisement display panel |  | 商品管理系统 Merchandise management |
| 单独选购配件 optional | 2000 G 咖啡豆盒（个） Coffee bean box, 2000 gram |  | 用户管理系统 CRM |
|  | 废水桶（个） Waste water bucket |  | 订单管理系统 Ordering management |
|  | 冲泡塑料装置（套） Brewing plastic device |  | 广告管理系统 Advertisement client management |
|  | 料盒（套）feed-in storage box |  | 活动管理系统 Promo activities management |
|  | 出料嘴（套）feed-out nozzle |  | 统计分析系统 Statistic management |
|  | 浆料罐（个）flavors storage vessel |  | 上网流量 Internet flow management |
|  | 外观塑料贴纸设计+安装（台） |  | 软件使用及系统空间 Software use and OS memory space |
|  | NFC刷卡功能（台） NFE card-swiping device |  |  |
|  | 纸币硬币投币功能（台） Coin and banknotes accepting device |  |  |