- Type	: MOTFON HA 100
- Shaft height	:	100mm
- Nominal power (mechanical):	1.1kW
- Speed	:	1500 rpm
- Food	: 230V three-phase 50Hz (D coupling)
- Carcass	:	Melting
- Tree	: 028mm — lg 60mm — steel (not exposed to sea water)
- Type of fixing	:	B5
- Brake	: 2Cn - Without release — 230Vac
- Ventilation	:	without (IC 410)
- Reheating	: 23OVac 25W
- Probes	: 3 PTC 155°
- Service	: S2 30min
- Ambient temperature	: 40°C
- Protection	:	1P67
- Paint	: C5M
- Certificate	:	Not applicable